## Slide 1: DREAM: Diabetic Retinopathy Analysis Using Machine Learning
Sohini Roychowdhury, Student Member, IEEE, Dara D. Koozekanani, Member, IEEE,
and Keshab K. Parhi, Fellow, IEEE
IEEE Journal of Biomedical and Health Informatics
Surabhi S Nath Suril Mehta Vishal Raj Dutta
2016271 2015104 2015115
GROUP 3

## Slide 2: CONTENTS
Topic Overview - Diabetic Retinopathy
Paper Abstract
Methodology Adopted
Stage 1
Stage 2
Stage 3
Results Obtained
Challenges Faced
Possible Extensions

## Slide 3: TOPIC OVERVIEW
Overview
Abstract
Methodology
Stage 1
Stage 2
Stage 3
Results
Challenges
Extensions

## Slide 4: PAPER ABSTRACT
Analyze FUNDUS images
Public datasets
  DIARETDB1 - 68 Images, MESSIDOR - 1200 Images
Apply Machine Learning techniques
  GMM, kNN, SVM, AdaBoost
Feature Reduction
Two-step Hierarchical Classification
Diabetic Retinopathy Severity Score generation
Beaten the best reported results
Overview
Abstract
Methodology
Stage 1
Stage 2
Stage 3
Results
Challenges
Extensions
Notes: Analyze FUNDUS images - FUNDUS images are photographs of the back of the eye - ie, the retina region

## Slide 5: METHODOLOGY ADOPTED
Stage 1:
Image Segmentation
Stage 2:
2-Step Hierarchical Lesion Classification
Stage 3:
Diabetic Retinopathy Severity Grade
GRADE 0 - No Diabetic Retinopathy
GRADE 1 - Mild Diabetic Retinopathy
GRADE 2 - Moderate Diabetic Retinopathy
GRADE 3 - Severe Diabetic Retinopathy
Remove Background
  Optical Disk
  Blood Vasculature
Identify Candidate Bright and Red Lesions
Candidate Bright Lesions
Candidate Bright Lesions
True Bright Lesions
True Red Lesions
Non Lesions
Cotton Wool
Spots
Hard
Exudates
Micro-
aneurysms
Hemorrhages
Overview
Abstract
Methodology
Stage 1
Stage 2
Stage 3
Results
Challenges
Extensions

## Slide 7: METHODOLOGY - Preprocessing
Overview
Abstract
Methodology
Stage 1
Stage 2
Stage 3
Results
Challenges
Extensions
Green plan Igreen chosen since maximum contrast
Histogram equalization
Contrast enhancement
Pixel scaling
Sharpness, Illumination enhancement
Laplacian, Gaussian filter
Median filtering

## Slide 8: METHODOLOGY - Stage 1
Overview
Abstract
Methodology
Stage 1
Stage 2
Stage 3
Results
Challenges
Extensions
Minimum Intensity, Maximum Solidity Algorithm to detect Optical Disk
  Intersection of red and bright regions
  Optical Disk has low intensity due to thick blood vessels and high solidity or compactness
Blood Vasculature detected
  Gradient smoothening
  Shade correction
  Extract largest red region
Detect candidate bright and red lesions as foreground
Mathematically:
Optical
Disk
Blood
Vasculature

## Slide 9: METHODOLOGY - Stage 2
Overview
Abstract
Methodology
Stage 1
Stage 2
Stage 3
Results
Challenges
Extensions
30 features were selected from 78 features using Adaboost
They included 14 structural features and 16 statistical features
GMM, kNN, SVM and their combination were used for hierarchical classification
Trained on DIARETDB1 with 21 images, 68 for internal testing

## Slide 10: METHODOLOGY - Stage 3
Overview
Abstract
Methodology
Stage 1
Stage 2
Stage 3
Results
Challenges
Extensions
Diabetic Retinopathy Severity Grading
Uses only red lesion numbers - more severe, needs to be more accurately detected
For bright lesions, false positives imply abnormalities other than Diabetic Retinopathy
  Must ensure low false positives, high specificity
For red lesions, false negatives will lead to false interpretation of Severity Grade
  Must ensure low false negatives, high sensitivity

## Slide 11: RESULTS OBTAINED
Overview
Abstract
Methodology
Stage 1
Stage 2
Stage 3
Results
Challenges
Extensions
Results on Internal Dataset - DIARETDB1
  Favourable classification of bright vs red lesions
  Sensitivity = 95%, Specificity = 90% for Micro-aneurysms vs Hemorrhages
  Sensitivity = 99%, Specificity = 97% for Cotton Wool Spots vs Hard Exudates
  Higher Specificity for Bright Lesions and higher Sensitivity for Red Lesions, as was desired
Results on External Dataset - MESSIDOR
  Sensitivity = 100%, Specificity = 53.16%, AUC = 0.904
  Beat state of the art Sensitivity = 96%, Specificity = 51%, AUC = 0.875 and outperformed all existing methods on MESSIDOR

## Slide 12: CHALLENGES FACED
Optical disk not blocked
  Additional Bright Lesions
Errenuous Image segmentation
  Inaccuracies in lesion classification
False detection of Bright Lesions does not affect Severity Score
  Cannot conclude accuracy on the basis of Severity Score accuracy
Retinal vein occlusions/degenerated retina
  Classified as abnormal though no Diabetic Retinopathy
Unbalanced datasets in Stage 2
  Biased classification
Overview
Abstract
Methodology
Stage 1
Stage 2
Stage 3
Results
Challenges
Extensions
Notes: Retinal vein occlusions - blockage of veins that carry blood away from the retina. Therefore eye looks red.
Degenerated retina - Retina deteriorates due to cell death

## Slide 13: POSSIBLE EXTENSIONS
Increase the training data
Apply Neural Networks
Test on multiple datasets
Overview
Abstract
Methodology
Stage 1
Stage 2
Stage 3
Results
Challenges
Extensions

## Slide 14: REFERENCES
https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=6680633
https://ieeexplore.ieee.org/document/6489310
http://www.ijo.in/article.asp?issn=0301-4738;year=2016;volume=64;issue=1;spage=38;epage=44;aulast=Gadkari
https://www.geographyandyou.com/population/health/expansion-eye-health-services-essential-combating-diabetic-retinopathy/
https://www.google.co.in/search?q=diabetic+retinopathy+india&ei=YLG3W8HCEMLe9QOT-YhI&start=10&sa=N&biw=1517&bih=730
https://drc.bmj.com/content/2/1/e000005